## Slide 1: Revolutionary Materials Processing
Dennis M. Bushnell
Chief Scientist
NASA LaRC

## Slide 2: Materials Processing
Alters the shape and/or the composition/properties of a material or an object, “transformation of input materials into a product”
In the current/ conventional case produces inclusions, dislocations, micro cracks which degrades strength by a factor of 20ish.
Is shifting in real time from “cutting” to Accretion
Is far more of an empirical art than a scientific technology [ e.g. physics/ chemistry of nano tube formation still unknown]

## Slide 3: The Usual Materials Processing Approaches
Thermal, incl. via lasers
Chemical
Pressure
Impact
Microwave
Ion Beam
Mechanical “Cutting”/Shear
Ultrasound
Microgravity
Explosive Forming
‘Flow” Processes
Electric Fields

## Slide 4: Revolutionary Materials Processing Approaches
Controlling material properties at the NANO Scale……By assembling at the Nano scale
‘Printing” writ large, any way or how, “additive manufacturing” [ on the way to atom-by-atom Molecular Manufacturing]
Production of “Nano Tubes”, other Nano Materials, e.g. Graphene etc.
Ionizing Radiation, High Strength Magnetics, Plasma, Bio processes, LENR, Fast to Explosive Shear/Compression
Quantum State Modification….., LENR Transmutations

## Slide 5: The usual, current approach to materials processing is to utilize one or perhaps two of the techniques. There are no extant cases discovered wherein multiple [ up to the some 17 methods available] were applied either sequentially of simultaneously. There are some 17! Possible combinatorials. Such combinations could/ should produce materials with quite different and possibly interesting properties, worth exploring this terra incognita, both experimentally and computationally…….

## Slide 6: As an example of what combinational processing approaches can produce, the combination of shear and compression has [ from both theory and experiment] collapsed electronic band gaps and produced materials with several orders of magnitude faster , and cold, chemistry, a superb spark plug.This field of energetics is termed Structural or Strain Bond Energy Release [ SBER]. Also, such combinations produce, for cracks, E-M emissions suitable for NDE evaluation, used on assembly lines in parts of Asia.

## Slide 7: Some Potential Materials Processing “Maidens Prayers”, Revolutionary Outcomes
Structural Nano tubes, contiguous tube assemblages that exhibit the strength of the individual tubes, order[s] of magnitude above that of usual materials.
“Ageless Materials”, Resultant materials which lack the usual collection of dislocations, nano cracks, inclusions etc. that degrade the properties of conventional materials.
Trabecular Bird Bone Etc. Structural Members

## Slide 8: Potential “Ways Forward” for ‘Ageless Materials”
Printing, ala work at “Livermore” at a scale above, but close as feasible to molecular manufacturing, with extreme care taken to control material micro/ nano structure
Combinatorial Materials processing approaches, which/ what TBD

## Slide 9: Potential Ways Forward for Structural Nano Tubes
Determine the physics, chemistry etc of the nano tube formative processes and investigate such for potential alterations which could produce far better materials than the current nano tube composites
Combinational Materials Processing approaches, Which/ What TBD
“Zipper Mechanism”, Stone-Wales bond rearrangements [rotations], merging of smaller tubes into larger ones
Applying Electron Beams at elevated Temperature, Frenkel pair defects/ covalent links
Interstitial B atoms, acting as “atomic Welders”…..
Combined external stimuli/ tuned molecular designs

## Slide 10: In the process of conducting such Revolutionary Materials Processing research, which is on the frontiers of the current SOA, we should discover, stumble over, unearth, produce materials with very different and possibly extremely useful properties, characteristics. [ Ala Goodyear and his discovery of the vulcanization of rubber]. Need to, for each new combinational result, determine the characteristics of the resultant materials.

## Slide 11: Of Interest….
DARPA ‘Atoms to Product” Project, Creating Manufacturing, Materials processing approaches between Nano and current industrial practice[ E-9 to E-3 meters].
The Livermore work , creating/ Printing assemblages of ever smaller discrete structural elements [ ordered micro-structure]
Materials “design” [ and fabrication?] at the Quantum level, Also via Machine learning technologies/ “Big Data”…and ab initio design incl. solid-to-solid transformations

## Slide 12: Some Additional Opportunities wrt Materials Design/ Processing - 1
Syn Bio/ Bio extraction, processing, fabrication/ products, NASA ARC has excellent efforts on all aspects of this putative “New Age” in materials. If utilize for Mars ISRU can adopt the Russian Design approach of clunky, add thickness/ weight where needed as do not have to haul the stuff from Earth.

## Slide 13: Some Additional Opportunities wrt Materials Design/ Processing - 2
Nano Inclusions in Materials to produce multifunctional materials that , instead of degrading, IMPROVES the material performance/ cost/weight/maintenance as add structural strength/ endurance, sensing, actuation, computing, energy storage [ chemicals, electrical]