## Slide 1: Machine Learning Applications in Aerospace System Design
Prof. Dimitri Mavris
Director, Aerospace Systems Design Laboratory (ASDL)
Langley Distinguished Regents Professor
Boeing Regents Professor for Advanced Aerospace Systems Analysis
School of Aerospace Engineering
Georgia Institute of Technology

## Slide 2: Presentation Outline
Introduction
  The Aerospace Applications landscape
  Our ‘machine learning’ perspective
Enablers for Aerospace Systems Engineering, Integration, Analysis and Design
Leveraging metamodeling to enable Design Space Exploration and Parametric Interactive Decision Making
Representative Case Studies

## Slide 3: Aerospace Applications Landscape
System of Systems Engineering
MDA/O enabled by Surrogate Modeling, Adjoint Method, and Variable Fidelity Strategies
Computational
Engineering
Operation-Centric, Larger-Scale SoS
Rapid Prototyping
with 3D Printing
Time Dependent Data and Model- driven Analysis of Cyber-physical Systems
“Digital Thread”
Data and Visual Analytics for Ultra-High Dimensional Space Exploration
Robust Design under Uncertainties
Uncertainty Quantification & Management
Disciplinary Analysis

## Slide 4: What is needed to enable these activities?
Transition from a single-discipline to a multi-disciplinary analysis, design and optimization perspective
Integration and Automation of the resultant design processes
Transition from a reliance on historical data to physics-based, variable fidelity formulations, especially true for unconventional concepts
Means to perform requirements exploration, technology infusion trade-offs and concept down selections during the early design phases (conceptual design) using these physics-based methods
Methods which will allow us to move from deterministic, serial, single-point designs to dynamic parametric trade environments
Incorporation of probabilistic methods to quantify, assess risk
Transition from single-objective to multi-objective optimization
Need to speed up computation to allow for the inclusion of variable fidelity tools so as to improve accuracy
Incorporation of advances in HPC, IT, M&S, machine learning and visual analytics (NASA CDT initiative) to support technology development, uncertainty burn down and decision making

## Slide 5: Aerospace Systems Engineering, Integration, Analysis & Design
Enabled by the advancement in
  Computational power
  Modeling & Simulation techniques
  Machine learning
Aerospace Engineering
Machine
Learning
System Engineering
Aircraft Design Methods
Design Trade-off Analysis
Technology Assessment, Selection and Forecasting
Multi-Physics Analysis
Unconventional Design Concepts
Vehicle Modeling & Calibration
…
Advanced System Analysis
Modeling & Simulation
Analysis of Alternatives
Concept Space Exploration
Optimization Techniques
Multidisciplinary Design Analysis & Optimization (MDAO)
Risk & Uncertainty Mitigation
Reliability Analysis
Requirement Analysis
Decision Making
…
Bayesian Inference
Probabilistic Design
Uncertainty Quantification & Management (UQ&M)
Artificial Neural Networks
Deep Learning
Kernel-Based Methods
Reasoning under Uncertainties
Dimensionality Reduction
Visual Recognition
Data Clustering
…

## Slide 6: What is Machine Learning?
“Machine learning” is a field of computer science that uses statistical methods to create programs that detect patterns in massive amounts of data that humans would be unlikely to find. It is the study of algorithms that infer the function they compute from example data
“Big Data” is it’s own world of tools, technologies, and solutions to accommodate large volume, high velocity and great variety in big data
“Data Mining” is related to any tool involved in excavating useful insights from data, big or small. While machine learning is focused on solving specific tasks, data mining is more exploratory term
Five major schools of thoughts in machine learning
  Symbolism: Inversed Deduction, Decision Trees
  Connectionism: Neural Networks, Deep Learning
  Evolutionism: Genetic Algorithm, Genetic Programming
  Bayesianism: Bayesian Networks
  Analogism: Kernel-Based Methods, Support Vector Machines
Source:
[Pedro Domingos, 2012]
“Civilization advances by extending the number of important operations we can perform without thinking about them.” Alfred North Whitehead

## Slide 7
Machine Learning Techniques
START
ANOMALY DETECTION
Linear and non-Linear Multivariate Regressions
CLUSTERING
TWO-CLASS CLASSIFICATION
MULTI-CLASS CLASSIFICATION
Predicting
categories
Discovering structure
Predicting values
Finding unusual
data points
Two
Three
or more
Adapted from Microsoft Azure Machine Learning: Algorithm Cheat Sheet

## Slide 8: Metamodeling for Design Space Exploration and Parametric Interactive Decision Making
Potential strategies to meet the computational challenges in MDO*
  Surrogate Modeling
  Variable Fidelity Approach
  Adjoint Methods
  (These are not necessarily mutually exclusive)
* National Research Council, “Decadal Study for Civil Aeronautics: Foundation for the Future,” 2006
** Missile picture from Nielsen Engineering and F-18 from AIAA
A Big Picture
Topological Exploration
Parametric Exploration near Baseline Design
Reduced-Order Model
High-Fidelity M&S Tools
Scope of Design Space
Model
Fidelity
MDO with Reduced Order Models
High-Fidelity Analysis within Restricted Design Space
High-Fidelity
Design Optimization
Pareto Frontier of Computational
M&S Capability
Variable Fidelity Approach*
Adjoint Methods*
Surrogate Modeling
the use of statistical techniques to build approximations (meta-models) of expensive computer analysis codes to facilitate multidisciplinary, multi-objective optimization and concept exploration [Simpson et al., 2001]

## Slide 9: Evolution of Adaptive Regression Techniques
Curse of Dimensionality
Linear Regression Methods (such as RSM)
Linear combinations of fixed basis functions
Linear parametric model
Kernel Based Method (such as Kriging / Gaussian Process)
Memory-based methods which store training data for prediction phase
Use similarity metrics for training vectors
Fast to train but slow at making prediction
Relevance Vector Machine
Perceptron
Used a layer of hand-coded features and tried to recognize objects by learning how to weight these features
Fundamentally limited in what they can learn to do
Hopfield Net
Support Vector Machine
Defining basis functions centered on the training data points, then, select a subset of them
“In 1990s, many researchers immigrated to SVM from MLP due to better performance.” [Hinton, 2007]
Boltzmann Machine
Deep Belief Net
“The Next Generation Neural Network” [Hinton, 2007]
Based on Restricted Boltzmann Machine
Synthesis between neural net and Bayesian net
Applied to the most challenging machine learning tasks today
Non-parametric Techniques
Add basis function for each of whole or partial training data
Originated from weight-kernel duality
Fast to train but slow prediction in general
Parametric Techniques
Use parametric forms for basis functions whose parameter values are adapted during training
Originally inspired by biological neural network
Hard to train but predicts fast
Nonlinear parametric model
Consists of multiple layers
Compare outputs with correct answer to get error signal
Back-propagate error signal to get derivatives for learning
Multilayer Perceptron

## Slide 10: Machine Learning/Surrogate Modeling
Key enabler that has allowed us to:
  speed up processes,
  protect proprietary nature of codes used,
  overcome organizational barriers (protectionism of tools and data),
  allow for the frameworks to be tool independent (no need for direct integrations of codes; also enables our desire for variable tool fidelity formulations),
  allow the designer to perform requirements exploration, technology infusion trade-offs, and concept down selections during the early design phases (conceptual design) using physics-based methods
Surrogate models can also be used at the integrated system level to determine responses at that level. This will allow us to move from deterministic, serial, single-point designs to dynamic parametric trade environments.

## Slide 11: Representative case studies

## Slide 12: Representative Case Studies
Metamodeling for Technology-Driven Design Space Exploration - Environmentally Responsible Aviation
Parametric, Physics Based Modeling - Kriging and Neural Net Metamodeling for Multi-Fidelity Aerodynamic Prediction (back up)
Probabilistic Design - Uncertainty Quantification using Bayesian Belief Net for Structural Optimization (back up)
Health Monitoring of Cyber-Physical Systems -Dynamic Data and Model-Driven Case Study
Manufacturing Influenced Design - Digital Factory of the Future: Data-Driven Production Planning & Control

## Slide 13: Metamodeling for Technology-Driven Design Space Exploration - ERA

## Slide 14: Environmentally Responsible Aviation (ERA) Program
NASA launched the ERA program to identify and mature technologies in the N+2 time frame that could impact a set of aspirational environmental goals
The objective was to not just meet the three goals separately, but simultaneously
Identifying appealing technology portfolios that could potentially simultaneously meet the goals required a design space exploration conducted on a physics-based M&S environment
GT-ASDL was tasked to aid NASA and its industry partners with this technology exploration
Noise
(cum below Stage 4)
-60%
-75%
better than -75%
-33%
-50%**
better than -70%
-33%
-50%
exploit metro-plex* concepts
N+1 = 2015***
Technology Benefits Relative
To a Single Aisle Reference
Configuration
N+2 = 2020***
Technology Benefits Relative
To a Large Twin Aisle
Reference Configuration
N+3 = 2025***
Technology Benefits
LTO NOx Emissions
(below CAEP 6)
Performance:
Aircraft Fuel Burn
Performance:
Field Length
-32 dB
-42 dB
-71 dB
CORNERS OF THE
TRADE SPACE

## Slide 15: Metamodeling for Environmentally Responsible Aviation
NASA ERA Dashboard
Goal: Dynamically (interactive, parametrically) evaluate technology implementation scenarios at the vehicle and fleet levels in a cohesive tradeoff environment
Features:
  Provide users with fast and visual feedback on aircraft and system-level metrics
  Ability to perform rapid trades and ‘what if’ scenarios in a manageable time
  High computation speed at both vehicle and system-level
  High combinatorial space (e.g. 40 technologies correspond to 1.1 trillion combinations)
Technology Evaluation Process:
Three hierarchical levels at which technologies are evaluated were incorporated in the ERA strategic planning and prioritization dashboard

## Slide 16: Modeling and Simulation Environment
Environmental Design Space (EDS)
  An M&S environment developed with support by the FAA/AEE to model existing aircraft as well as advanced technologies and concepts
EDS integrates continuously updated NASA design tools with industry vetted design logic to provide a parametric aircraft design capability
  Consistent engine to airframe match
  Creates output links to connect with fleet assessment tools
  Takes advantage of years of development and validation by NASA
EDS provides integrated analysis capability to estimate:
  Source noise
  Exhaust emissions
  Engine and vehicle performance

## Slide 17: Analysis Procedure
Vehicle assessment method combines technology impact modeling with vehicle modeling, sizing and synthesis to evaluate performance metrics
Technology impacts are modeled at component level
  Allowed to propagate through EDS in order to determine the system level benefits
Utilizes surrogate modeling to evaluate technology trade space for multiple vehicle configurations and classes
“k-factor” Approach
Quantitative forecasting requires quantitative representation of technologies
Technologies, or potential impacts of technologies, can be defined as delta's with respect to a current system baseline
``k-factors'’ directly modify computed metrics during the analysis process, which in turn simulate technology benefits and penalties

## Slide 18: EDS Vehicle Calibration
EDS Vehicle model classes
EDS vehicle models have been developed, calibrated, and validated to existing vehicle in the fleet. Rigorous vetting process with industry SMEs
EDS captures existing aircraft models from Regional Jets, RJs through Very Large Aircraft, VLA aircraft
Existing aircraft models serve as departure point for modeling new technology engines and aircraft

## Slide 19: Metamodeling for Environmentally Responsible Aviation
Metamodel Generation
Metamodels are used to enable the dashboard to rapidly evaluate metrics at each of the assessment levels
Metamodels are generated for each level:
  Vehicle performance from EDS (Vehicle)
  Noise contour surrogates (Airport)
  Fleet fuel burn and NOx surrogates (Fleet Level)
Each level of surrogates are consistent with the previous allowing for trade-off and understanding of interdependencies
  Vehicle surrogates are a function of technologies
  Airport surrogates are a function of technologies, airport properties and flight schedule
  Fleet level surrogates are a function of technologies, fleet mix, replacement schedule and operations

## Slide 20: Visual Analytics- Parametric, Interactive Sensitivity Derivatives

## Slide 21: Analysis of Variance – Relative Contribution Significance

## Slide 22: Global Space Exploration- Monte Carlo Analysis

## Slide 23: Visual Analytics- Multivariate Analysis- Filtered Monte Carlo

## Slide 24: Propagation of Vehicle Impact and Uncertainties to Fleet Level
AEDT: Aviation Environmental Design Tool
GREAT: Global and Regional Environmental Analysis Trade-off

## Slide 25: Example Fleet Results- Fuel Burn and Noise Contours
Output and results are visualized at both the vehicle system level and at a fleet-wide impact level
Provides insight on which technologies and configurations should be pursued in order to meet system level goals – whether it be fuel burn, emissions, noise, or a compromise between all three
Provides user with ability to manipulate fleet composition to observe effects on fuel burn and emissions
Compares impacts on airport noise contours for a generic runway configuration to give insight on how technologies reduce and reshape contours

## Slide 26: Visual Analytics and Decision Making for ERA
Probabilistic Analysis Supporting Decision Making Process
Multi-Objective Combinatorial Optimization
Visual Analytics with 3D Vehicle Rendering
Highly Interactive ‘Control Panel’ for ‘Virtual Experiments’
Instant Visualization of Design Space
Metamodeling enables instant queries for noise and emission performance in vast combinatorial design space

## Slide 27: Dynamic Data and Model-Driven Application
Goal: a virtual M&S testbed for future campus energy technologies that
  Use existing meter data & expertise of GT Facilities
  Address GT Administration energy goals & planning needs
  Facilitate “what if?” gaming, scenario evaluation, & trade studies

## Slide 28: Dynamic Data and Model-Driven Application
1
2
3
4
5
Basic model construction for various load items using up-to-date machine learning algorithms
Construction of integrated M&S environment and validation of it using historic operation data
Execution of Design of Experiments to identify optimal plant setting parameters
Validation of optimal plant setting parameters against historic data
Application of data-driven models on M&S environment to perform Virtual Experimentation and to improve plant operation
Table of weather condition and corresponding optimal setting*
Dymola Model for GT CW System
Dymola versus Historic Data
Potential Energy-Saving using the previously identified optimal setting
Neural Net Model for Cooling Load versus Historic Data
GT FORESIGHT as a testbed for Data-driven Campus Utility Operation Research
28

## Slide 29: Dynamic Data and Model-Driven Application

## Slide 30: Deep Learning for Building Energy Consumption
1. Raw Data
2. Annual Trend Extraction
3. Daily Usage Pattern Identification
Useful Preprocessing Logic Developed
Each building has a unique signature energy usage pattern
ION Database
Decoupled Modeling for Usage Pattern and Quantities

## Slide 31: Production Planning & Control towards Smart Factory
Research objective: Support schedule recovery by identifying reactive scheduling strategies that mitigate the impact of delays and disruptions
Requires to
  Generate a more realistic predictive schedule (include disruptions)
  Identify the system-wide impact of selecting a specific plan, encountering a disruption, and/or implementing a mitigation strategy
Drilling System
Cycle time prediction
Analyze data to further identify relevant parameters driving cycle time
Identify appropriate sample size and samples
Apply a variety of nonlinear/adaptive models to fit cycle time
Conduct a comprehensive trade study to finalize prediction model and procedure
Improve reliability and accuracy in 'cycle time' prediction
Disruptions prediction
  Identify where issues in the automated drilling sequence lead to increases in cycle time
Develop disruption prediction model
Simulation at System (cell) and System of Systems (building) Levels
Develop a physics-based model that integrates the data-driven model generated for the drilling operations
Calibrate, verify, and validate model(s) using historical data
Forecasting & Impact Assessment
Provide the user with a set of recovery scheduling strategies that minimize the impact on metrics of interest (Flow time, etc.) and risk (schedule variation)

## Slide 32: Production Planning & Control towards Digital Factory of the Future
Sequential Flow Analysis
Anomaly Detection
Decision Support
Process Layer
Manufacturing Scheduling
Process Monitoring
Process Feature Analysis
Energy Layer
Consumption Minimization
Energy Usage Monitoring
Demand Modeling
Logistics / Supply Chain Layer
Material Control System
Delay Analysis
Agent-Based Supply Chain Modeling
Potential Applications of Data Analytics Towards Implementation of the Digital Factory
*All task elements are interrelated.

## Slide 33: Vision of Data-Driven Airspace Operation
Dynamic Case-Based Reasoning system for integrated diagnosis of the National Airspace System

## Slide 34: Closing Remarks: The Vision for the Future -Virtual Experimentation
A game-changing, cyber-physical initiative that will enable the capability to seamlessly integrate and deploy
technologies into the analysis, design, testing, validation, discovery, and manufacturing processes

## Slide 35: Depiction of an Integrated Virtual Experimentation Environment
‘Selection’ of suitable Codes & Tools
Instant Construction of ‘Virtual Facilities’
Advanced Integration based on ‘Virtual Machines’
Adaptive Simulation Runs over Multiple Disciplines
Data Analytics to Monitor ‘Virtual Experiments’
Parametric Task Designer
Interactive Control for Every Detail of ‘Virtual Instruments’
Visual Analytics as ‘Experiment Reports’

## Slide 36: Back up Slides

## Slide 37: Probabilistic Aero-Structural Analysis
Aircraft designers must set design (target) loads for structural optimization
  Challenges
    Large number of flight conditions ~ 106
    High degrees of Uncertainties (from design immaturity, sparseness in data, biases in analysis codes, etc.)
  Goal
    Perform Uncertainty Quantification (UQ) by focusing to important flight conditions while properly considering dependencies among sources of uncertainties
  Enablers
    Bayesian Adaptive Sampling for efficient sampling
    Bayesian Belief Network for dependency/covariance quantification
Weight
Aero
Structure
Design
Stresses
Probability
ε1
ε2
ε3
?
  Overestimation  excess weight
  Underestimation  costly re-design
ε2 = Uncertainties in analysis results (CFD*) are properly updated by BBN as evidence (Wind Tunnel Test) is successively provided.
ε1 = Uncertainties in payload and fuel weight, etc.
ε3 = Uncertainties in material properties such as stiffness
Loads

## Slide 38: Probabilistic Aero-Structural Analysis
Bayesian Network
  A probabilistic graphical model (a type of statistical model) that represents a set of random variables and their conditional dependencies via a directed acyclic graph (DAG)
    Integrate data from different sources
    Accounts for dependencies
    Probabilistic surrogate modeling
    Uncertainty quantification & propagation
    Uncertainty management & reduction
Bayesian Network using UNINET
  Support non-parametric continuous, discrete distribution variables and functional nodes
  Network Building
    User defined model
    Automatic network generation from data
      Pruning process
  Dependency modeled through rank correlation and realized using Gaussian Copula
  Sampling
    Analytic real time sampling for probabilistic nodes
      Use vine copula and Gaussian copula dependence
    Sample based conditioning: For Network with functional nodes
  Additional features
    Sculpting
    Visualization: UNIGRAPH
    Sensitivity analysis: UNISENS
Continuous/Discrete variable nodes & Functional nodes in UNINET
Networks before & after pruning
Posterior distribution after conditioning on ‘V7’

## Slide 39: Probabilistic Aero-Structural Analysis
Bayesian adaptive sampling for deterministic scenario
Bayesian adaptive sampling for non-deterministic scenario
Adaptive sampling for 99% percentile load
Optimized weight at different reliability level
Goal achieved

## Slide 40: Metamodeling for Aerodynamic Shape Optimization
Creation of Metamodels of Euler-level aerodynamics for a parametric vehicle outer model line (OML) for rapid design space exploration
  Massively parallel 580,000 runs by computational nodes in the multiple DoD HPC Centers
    Fully parametric OML design variables
    Total 48 Flight Conditions with various Mach numbers (0.3~4.0), Angles of Attack (0/15/40), and Sideslip Angles (0/5/15)
    An inviscid CFD package, Cart3D
    1.5M~2.5M Computational Grid Cells for each case
  RSM, polynomial NN, ANN, RBFN techniques tested
  Neural Networks used as final metamodels for three Force and three Moment Coefficients
    Three Force Prediction used as input when training for moment coefficients
Finding a needle in haystack
Design Variables for Fully-Parametric Outer Mold Line
Example of CFD Result
Example of NN Fit Result
Summary of Metamodeling Results

## Slide 41: Metamodeling for Multi-Fidelity Analysis
Multiplicity in Data Sources
  Readily obtainable, but lower-accuracy sources (e.g., reduced-order analysis)
  Higher-accuracy, but computationally expensive sources (e.g., wind tunnel experiment results, high-fidelity analysis)
Universal Kriging has advantages
  For multi-fidelity modeling, lower-accuracy (cheap) data source can be used to identify general trends, while the higher-accuracy (expensive) source to correct the metamodel
  For adaptive sampling, it is straightforward to estimate potential reduction in the prediction variance for candidate sample points
Ghoreyshi Co-Kriging for Multi-Fidelity Metamodeling
  Additional to training data for single Kriging, ycheap data serve as an extra input parameter
  The objective is to accurately predict yexpensive for unseen cases
Adaptive Sampling
  Efficient estimation of prediction variances based on Schur’s complement formula for candidate samples
Demonstration on Pitching Behavior Prediction for Reusable Winged First-Stage Boosters
  Design Requirement: Maintaining sufficient control authority for a wide range of flight condition
  Conceptual design fully accounting for control characteristics is extremely challenging due to the need for high-fidelity analyses that, in general, are computationally prohibitive for vast parameter space in early design phase
  Multi-Fidelity Metamodeling with Adaptive Sampling brought down computational cost significantly serving the goal
Bringing-Down Computational Cost Even More by Adaptive Sampling